## Slide 1: Infrared Sensing Multi-Function High-Brightness LED Light that Can Be Charged by Indoor Bulb Light and Outdoor Sunlight
American-Made Solar Prize Round 2

## Slide 2
Background:
At present, solar lights on the market can only be charged by sunlight, while indoor-used infrared sensing LED lights are powered by AC or batteries. Solar lights can only be used outdoors. Indoor AC-powered LED lights stop working when AC power is off, and battery-powered LED lights are generally low brightness due to battery capacity.

## Slide 3
The invention has the advantages of the outdoor solar lamp and the indoor infrared sensor lamp, It can be charged by sunlight or bulb light in the room. It is convenient to use, energy saving and environmental protection.

## Slide 4
This infrared sensor lamp is composed of :
1.a PV panel,
2.a polymer lithium battery.
3.an infrared sensor head,
4.an amplifier and control circuit,
5.a charge management circuit,
6. LED lights.

## Slide 5
With the pefect design, we integrate circuits to this small PCB board.

## Slide 6
A pyroelectric infrared sensor, model RE200B-P, which together with the Fresnel Lens form a Passive Infrared Sensor Head.

## Slide 7
This LED light uses a round PV panel with a diameter of 90 mm, which working voltage is 5.5 volts and the charging current is 120 mA.

## Slide 8
12 LEDs (model 3528) makes it very bright.

## Slide 9
The infrared sensor lamp is placed under the chandelier, and the PV panel faces the LED bulb.

## Slide 10
The infrared sensor light is charging when bulb is lit.

## Slide 11
When the infrared sensor light detects an object moving within 30 inches at night, it will automatically light up.

## Slide 12
Adjust the direction of the sensor head to select the area to trigger. When the person gets up at night, it automatically lights up and when the person returns to the bed, it automatically goes out.
It's safe and conveinent for elderly and children to get up for bathroom at night.

## Slide 13
A special IC for lithium battery charge management is on the board.
This versatile LED light with infrared sensor can be efficiently and safely charged by sunlight or indoor bulb light.

## Slide 14
This sensor light can be used as a camping light in the tent，especially suitable for children's camping.

## Slide 15
It is simple to install, safe and convenient to use, and maintenance-free.
It is a new energy-saving and environmentally friendly family night light, emergency light and outdoor camping light.

## Slide 16: NEWSOLARZONE LLC.
NEWSOLARZONE LLC. was founded in 2017 in Nashville, TN.
The company's goal is to use clean and renewable energy to develop high-tech and environmentally friendly home appliances and public products for the benefit of our healthy life and protect our planet.
Since the establishment of the company in 2017, we have developed a number of innovative patented products that are gradually being introduced to the market.
We believe that as long as we work together, the sky will be bluer, the grass will be greener, the water will be cleaner, the air will be fresher, our life will be happier and healthier, and our planet will be more beautiful.