## Slide 1
Hybrid PV panel has modified glass entrance sheet that efficiently separates the direct sunlight and diffuse sky components of solar energy
  Direct sunlight component focused onto mm-size multijunction PV cells, 43% - 50% efficient, mounted on silicon cells
  Diffuse sky and backlight components transmitted to the 20% efficient Si cell
Set! demo prototype shown is a working 3” section of a full-scale module. Energy output to be compared in the field to the same Si cell alone
Overcomes the fundamental losses of previous “CPV” solar. Close ≥ 100% energy output gain over a wide range of solar resource
Good potential for lower LCOE than silicon PV
A practical way to double the output of PV panels
Projected energy gain vs Si on single axis Phoenix Kansas City New York City
115% 105% 95%
Demo will have an entrance window of glass formed as a 4x4 array of 18 mm square lenses
Side mirrors in the demo will ensure full response to diffuse rays at all angles, as in full 1 m x 2 m panel with same size lenses
Roger Angel
Zach Holman
Nick Didato