## Slide 1
Team Name: | Clean Carbon Conductors
Primary Submitter Name: | Dmitri Tsentalovich
City and State: | Houston, TX
Member Names (including partners and affiliates): | DexMat, Inc.- Dmitri Tsentalovich, Colin Young, Tyson LaRochelle, Bryan Hassin, Sofia Izaguirre Rice University- Matteo Pasquali, Glen Irvin, Mitchell Trafford, Oliver Dewey, Lauren Taylor, Michelle Chaves, Ivan Sigueira, Steven Williams, JDT Consulting- Joe Trentacosta
Submission Title: | Clean Carbon Conductors
*A Public Document
Description of Material
Galvorn CNT conductors are composed of many highly aligned molecules known as carbon nanotubes (CNTs), which can be twice as conductive as copper
Current state-of-the-art Galvorn conductors are 6 times less conductive, but also 6 times lighter and 10 times stronger than copper
At the current rate of progress, Galvorn CNT conductors are on track to surpass copper conductivity within 5-10 years
Fabrication Approach
Galvorn fibers are produced by extruding solutions of CNTs through small holes and winding the resulting filaments under tension, very similar to the Kevlar production process
We expect to achieve significant conductivity improvements in Galvorn fibers by using significantly longer, defect-free CNTs, by improving CNT alignment in the fibers, and by electrochemically doping the constituent CNTs with halogen compounds
Potential Impact
Developing a CNT conductor that conducts as well as copper, while being 6 times lighter will revolutionize wire and cable for automotive, aerospace, power transmission, and electrical motor industries
CNT conductors can be produced with net-zero CO2 emissions and production will be cost competitive with copper at scale
Using CNTs over copper and aluminum could reduce CO2 emissions by 100’s MT per year
Notes: Public PowerPoint Summary Slide
Make a public-facing, one-slide summary using PowerPoint containing technically specific details that can be understood by most people. The slide will be made public and should include (1) the competitor or team name and team leader, (2) submission title, (3) description of material, (4) fabrication approach, and (5) potential impact. Please make any text readable in a standard printout and conference room projection. Please refer to the official CABLE Prize Rules Document for full requirements: https://americanmadechallenges.org/cable/docs/rules/CABLE_Prize_Official_Rules.pdf