## Slide 1
Innovating Distributed Embedded Energy Prize (InDEEP)
Introduction to Wave Energy 2.0
January 10, 2024
Notes: Bill

## Slide 2
Everyone is joined in listen-only mode
Audio Issues?—Try connecting over the phone
If that doesn’t work, visit the Zoom Help Center webpage
Q&A—Submit your questions using the chat box
Webinar Logistics
Notes: Brittany

## Slide 3: Agenda 1.0
Webinar 1. – April 26, 2023
Introductions
Ocean Waves
Wave Energy
Technology
Challenge & Motivation
Q&A
Webinar 2. – January 10, 2024
Introductions
Wave – Body Interaction
Wave Energy Conversion
Technology Development Methods
Technology Development History
Challenge & Motivation & Solution
Q&A
Agenda 2.0

## Slide 4
Introductions
Notes: Brittany

## Slide 5: Innovating Distributed Embedded Energy Prize
$2.3M prize pool
Three phases over two years
Incentivize progress in early-stage research
Help solve technical challenges that could be applied to wave energy

## Slide 6: Contributing to Leaderboard Scoring
For questions about the prize overall, view our recorded conversation on April 12 2023
Participation in this webinar contributes to your final leaderboard score
Make sure to complete the Leaderboard Eligibility Form to receive points for your participation
If you haven’t done this yet, do so now: https://www.herox.com/indeep
WPTO’s desired outcome for InDEEP is an understanding of the landscape of innovators and potential DEEC-Tec solutions that could be applied to wave energy devices.

## Slide 7
Ocean Waves

## Slide 8: Ocean Waves – Key Geometric Parameters
"Local wavelength" by Brews ohare - Own work
Licensed under CC BY-SA 3.0 via Commons
"Sine waves different frequencies" LucasVB. . Own work assumed
.. Licensed under Public Domain via Commons
"Sine wave amplitude" by Kraaiennest - Own work
Licensed under CC BY-SA 3.0 via Commons
wave height

## Slide 9: Ocean Waves – Key Temporal Parameter
World Meteorological Organisation: Guide to wave analysis and forecasting (WMO 702), 2nd
edn. WMO (1998)
Types of waves in the ocean by wave period

## Slide 10
Ocean Waves – Visualization of Dynamics
"Wave motion-i18n-mod" by Original uploader was Vargklo at en.Wikipedia
Licensed under CC BY-SA 3.0 via Commons
Motion of a particle in an ocean wave.
A = At deep water.
B = At shallow water
1 = Propagation direction.
2 = Wave crest.
3 = Wave trough.
Wikipedia

## Slide 11
Ocean Waves – Visualization of Dynamics
“Deep water wave” by Kraaiennest – Own work.
Licensed under GFDL via Commons
Notes: Brittany

## Slide 12
Ocean Waves – Visualization of Dynamics
“Deep water wave” by Kraaiennest – Own work.
Licensed under GFDL via Commons
Notes: Brittany

## Slide 13: Ocean Waves – Three Dimensions
From WAFO

## Slide 14
Wave – Body Interaction

## Slide 15: Forces on a Floating Body

## Slide 16: Forces on a Floating Body

## Slide 17: Hydrostatics – Restoring Force
Force as a Function of Displacement
Degrees of Freedom
  Heave – driven by water plane area
  Pitch – driven by water plane area, center of buoyancy and center of gravity
  Surge – Not occurring, neutral
Stability

## Slide 18: Wave Diffraction – Excitation Force
Force in the body due to the presence of the wave
Incident wave
  Froude Krylov
Scattered wave
Diffraction = Incident + scattered wave
Excitation
Degrees of Freedom

## Slide 19: Added Mass – Hydrodynamic Inertia
Force as a function of acceleration
Represents the inertia of the accelerated water mass
Frequency independent when body is deeply submerged
Frequency dependent when body is near water surface
Cross coupling effects between different degrees of freedom
Cross coupling effects between degrees of freedom of different bodies
Newman, Marine Hydrodynamics, 1977

## Slide 20: Added Mass – Hydrodynamic Inertia
Force as a function of acceleration
Represents the inertia of the accelerated water mass
Frequency independent when body is deeply submerged
Frequency dependent when body is near water surface
Cross coupling effects between different degrees of freedom
Cross coupling effects between degrees of freedom of different bodies
Newman, Marine Hydrodynamics, 1977

## Slide 21: Wave Radiation – Hydrodynamic Damping
Force as a function of velocity
Represents the energy consuming damping due to the radiation of a wave
Frequency dependent
Zero when body is deeply submerged
Cross coupling effects between different degrees of freedom
Cross coupling effects between degrees of freedom of different bodies
Newman, Marine Hydrodynamics, 1977

## Slide 22
Wave Energy

## Slide 23: Wave Energy – Propagation
Garrison, T.S.: Oceanography: An Invitation to Marine Science, 7th edn. Brooks/Cole,
Belmont, USA (2010)
Energy Flux
[kW/m]
Incident Power

## Slide 24: Wave Energy – Time and Frequency Domain
Massel, S.R.: Ocean Surface Waves: Their Physics and Prediction, 2nd edn. World Scientific
Publishing, Singapore (2013)
Super-positioning of waves (corresponding to spectral components) to create water
surface elevation (left) and the resulting spectrum (right)

## Slide 25: Wave Energy – Spectral Representation
https://wikiwaves.org/Ocean-Wave_Spectra
Real spectra (left) and parameterized (right) spectral representation
(JONSWAP and Pierson-Moskowitz spectra) – defining sea states

## Slide 26: Wave Energy – Distribution of Spectra
Matt Folley

## Slide 27: Wave Energy – Distribution of Spectra

## Slide 28: Wave Energy – Distribution of Orientation/Direction
Average directional spectral variance density (m2/Hz/rad) at the European Marine Energy, Centre, Orkney, Scotland
Matt Folley
Matt Folley

## Slide 29: Wave Energy – Resource
https://maps.nrel.gov/marine-energy-atlas/

## Slide 30: Wave Energy – Resource
https://maps.nrel.gov/marine-energy-atlas/
33 kW/m =
/(2 m)

## Slide 31
Wave Energy Conversion

## Slide 32: Energy Distribution
Single Mode Sea-State
Bi-Modal Sea-State

## Slide 33: Ocean Wave Dynamics – Dispersion Relation
Quick explanation
Formular
Graph
Meaning
Ref: https://folk.ntnu.no/oivarn/hercules_ntnu/LWTcourse/indexA.htm

## Slide 34: Wave Energy Absorption
Jorgen Hals

## Slide 35: Power Takeoff – Damping & Restoring
Power Take-Off Functions
  Provide interaction with the wave absorbers to extract energy from ocean waves and convert to other secondary energy form (e.g., mechanical)
  Convert the secondary energy form to the desired energy form (e.g., electrical)
Power Take-Off Capabilities
  Energy conversion through damping force – in phase with velocity
  Energy storage through restoring force – in phase with displacement

## Slide 36: From Wave Power to Power Matrix

## Slide 37: Wave Energy Absorption – Benchmark Study
Quantities of Interest
Performance Metrics

## Slide 38: Wave Energy Absorption – Benchmark Study

## Slide 39: Wave Energy Absorption – Benchmark Study

## Slide 40: Wave Energy Absorption – Benchmark Study

## Slide 41
Technology

## Slide 42: Technology – Concept Classification
Location
Orientation

## Slide 43: Technology – Concept Classification
Mechanism of Extraction

## Slide 44: Technology – Concept Classification
Reactional Reference
Motion Degrees of Freedom in Coordinate System

## Slide 45: Technology – Concepts

## Slide 46: Technology – Concepts

## Slide 47: Technology – Concepts

## Slide 48: Technology – Concepts

## Slide 49: Technology – Concepts

## Slide 50: Technology – Energy Conversion
A. Têtu
Different paths for wave energy to electricity conversion

## Slide 51
Technology Development Methods

## Slide 52: System Modelling and Simulation
Wide variety of system models and simulation tools to be selected for use case
More to come …

## Slide 53: Wave Basin Testing and Validation
Fundamental Concept
Power Absorption Code Validation
Survival Testing
Advanced Control Testing
Sophisticated Direct Generation Power Take-Off

## Slide 54: Bench and Laboratory Testing and Characterization

## Slide 55: Open Water Demonstration – Test Sites
EU
US: Hawaii & Pacific Coast

## Slide 56
Technology Development History

## Slide 57: Early Developments
First patent is reported to have been filed as early as 1799 by Girard and since then patent numbers are well in the thousands
First oscillating water column designed by Palme in 1920
Early developments in the US include 1898 patent by Wright

## Slide 58: Early Developments
First commercial application of wave energy:
In 1940s, Japanese inventor, Yoshio Masuda, lead substantial research and invented, designed and build floating of oscillating water column device to generate power for navigation buoys.
Commercialization in large numbers in Japan from 1965 and later in USA.

## Slide 59: Oscillating Water Column Devices

## Slide 60: Oscillating Water Column Devices

## Slide 61: Oscillating Water Column Devices

## Slide 62: Floating Oscillating Water Column Devices

## Slide 63: Oscillating Water Column Devices Turbines

## Slide 64: Salter Duck

## Slide 65: Salter Duck
Survivability
Ref: Salter, S. Wave energy: Nostalgic Ramblings, future hopes and heretical suggestions. J. Ocean Eng. Mar. Energy 2, 399–428 (2016). https://doi.org/10.1007/s40722-016-0057-3

## Slide 66: Salter Duck

## Slide 67: Salter Duck … Weptos

## Slide 68: Pelamis

## Slide 69: Pelamis

## Slide 70: Pelamis

## Slide 71
Challenges & Motivation

## Slide 72: Technology – Development Challenges: Cost

## Slide 73: Technology – Development Challenges: Risk

## Slide 74: Technology – Development Challenges: Time

## Slide 75: Technology – Development Challenges: Innovation

## Slide 76
Challenges & Motivation & Solutions

## Slide 77: Technological Evolution vs Intelligent Design
• Early convergence of concepts,
• Technical feasibility, industrial production and market opportunity at all and growing scales,
• Availability of technological knowhow & experience in theory, design, production & operation of very similar industrial applications,
• Cheap and easy access (onshore) to operating system, allowing gradual failure rate reduction during commercial operations.
Technological Evolution
Intelligent Design
• Large spectrum of different converter system concepts,
• Strongly decreased market opportunity at reduced scales,
• Limited transferability of technological experience, design, production and operation of similar industrial applications,
• Expensive and delayed access to operating system (offshore), prohibiting high failure rates from the onset of commercial operations.
Wind Energy
Wave Energy

## Slide 78: Learnings and Leads Solutions
Technology Development Strategy, Methods and Tools
  Development Protocols
  Cost, Time and Risk Reduction
Techno-Economic Assessment
Significant improvement in Modelling, Simulation of Dynamics, Loads and Stresses
System Optimization & Co-Design
Marine Operations Modelling
Novel Power Conversion Systems
Advanced Manufacturing Methods
Identification of Alternative Markets
  Blue Economy
  High Impact Applications
Design Paradigm Shifts

## Slide 79: Technology – Possibility for Paradigm Shift?
SBM Offshore
Pelamis

## Slide 80: Questions
Notes: Carrie