## Slide 1
Innovating Distributed Embedded Energy Prize (InDEEP)
Introduction to Wave Energy 3.0
August 27, 2024
Notes: Bill

## Slide 2
Everyone is joined in listen-only mode
Audio Issues?—Try connecting over the phone
If that doesn’t work, visit the Zoom Help Center webpage
Q&A—Submit your questions using the chat box
Webinar Logistics
Notes: Brittany

## Slide 3: Innovating Distributed Embedded Energy Prize
$2.3M prize pool
Three phases over two years
Incentivize progress in early-stage research
Help solve technical challenges that could be applied to wave energy

## Slide 4: Contributing to Leaderboard Scoring
For questions about the prize overall, view our recorded conversation on April 12
Participation in this webinar contributes to your final leaderboard score
Make sure to complete the Leaderboard Eligibility Form to receive points for your participation
If you haven’t done this yet, do so now: https://www.herox.com/indeep
WPTO’s desired outcome for InDEEP is an understanding of the landscape of innovators and potential DEEC-Tec solutions that could be applied to wave energy devices.

## Slide 5: Agenda 1.0
Webinar 1. – April 26, 2023
Introductions
Ocean Waves
Wave Energy
Technology
Challenge & Motivation
Q&A
Webinar 2. – January 10, 2024
Introductions
Wave – Body Interaction
Wave Energy Conversion
Technology Development Methods
Technology Development History
Challenge & Motivation & Solution
Q&A
Agenda 2.0

## Slide 6
Introductions
Notes: Brittany

## Slide 7
Presented by
Jochem Weber, National Renewable Energy Laboratory (NREL)
Matt Folley, Applied Renewables Research (ARR)
Daniel, Gaebele, Sandia National Laboratories (SNL)
Notes: Brittany

## Slide 8: Agenda 1.0
Webinar 1. – April 26, 2023
Introductions
Ocean Waves
Wave Energy
Technology
Challenge & Motivation
Q&A
Webinar 2. – January 10, 2024
Introductions
Wave – Body Interaction
Wave Energy Conversion
Technology Dev. Methods
Technology Dev. History
Challenge & Motivation & Solution
Q&A
Agenda 2.0
Webinar 3. – August 27, 2024
Introductions
Wave – Energy – Conversion
Technology Dev. Methods
Challenge & Motivation & Solution
Tuning, Bandwidth, Constraints
Conversion Chain Control Co-Design
Overall Objective
Q&A
Agenda 3.0

## Slide 9
Ocean Waves

## Slide 10: Ocean Waves – Key Geometric Parameters
"Local wavelength" by Brews ohare - Own work
Licensed under CC BY-SA 3.0 via Commons
"Sine waves different frequencies" LucasVB. . Own work assumed
.. Licensed under Public Domain via Commons
"Sine wave amplitude" by Kraaiennest - Own work
Licensed under CC BY-SA 3.0 via Commons
wave height

## Slide 11: Ocean Waves – Key Temporal Parameter
World Meteorological Organisation: Guide to wave analysis and forecasting (WMO 702), 2nd
edn. WMO (1998)
Types of waves in the ocean by wave period

## Slide 12
Ocean Waves – Visualization of Dynamics
"Wave motion-i18n-mod" by Original uploader was Vargklo at en.Wikipedia
Licensed under CC BY-SA 3.0 via Commons
Motion of a particle in an ocean wave.
A = At deep water.
B = At shallow water
1 = Propagation direction.
2 = Wave crest.
3 = Wave trough.
Wikipedia

## Slide 13
Ocean Waves – Visualization of Dynamics
“Deep water wave” by Kraaiennest – Own work.
Licensed under GFDL via Commons
Notes: Brittany

## Slide 14
Ocean Waves – Visualization of Dynamics
“Deep water wave” by Kraaiennest – Own work.
Licensed under GFDL via Commons
Notes: Brittany

## Slide 15: Ocean Waves – Three Dimensions
From WAFO

## Slide 16
Wave Energy

## Slide 17: Wave Energy – Propagation
Garrison, T.S.: Oceanography: An Invitation to Marine Science, 7th edn. Brooks/Cole,
Belmont, USA (2010)
Energy Flux
[kW/m]
Incident Power

## Slide 18: Wave Energy – Time and Frequency Domain
Massel, S.R.: Ocean Surface Waves: Their Physics and Prediction, 2nd edn. World Scientific
Publishing, Singapore (2013)
Super-positioning of waves (corresponding to spectral components) to create water
surface elevation (left) and the resulting spectrum (right)

## Slide 19: Wave Energy – Spectral Representation
https://wikiwaves.org/Ocean-Wave_Spectra
Real spectra (left) and parameterized (right) spectral representation
(JONSWAP and Pierson-Moskowitz spectra) – defining sea states

## Slide 20: Wave Energy – Distribution of Spectra
Matt Folley

## Slide 21: Wave Energy – Distribution of Spectra

## Slide 22: Wave Energy – Distribution of Orientation/Direction
Average directional spectral variance density (m2/Hz/rad) at the European Marine Energy, Centre, Orkney, Scotland
Matt Folley
Matt Folley

## Slide 23: Wave Energy – Resource
https://maps.nrel.gov/marine-energy-atlas/

## Slide 24: Wave Energy – Resource
https://maps.nrel.gov/marine-energy-atlas/
33 kW/m =
/(2 m)

## Slide 25: From Wave Power to Power Matrix

## Slide 26
Wave – Body Interaction

## Slide 27: Forces on a Floating Body

## Slide 28: Forces on a Floating Body

## Slide 29: Hydrostatics – Restoring Force
Force as a Function of Displacement
Degrees of Freedom
  Heave – driven by water plane area
  Pitch – driven by water plane area, center of buoyancy and center of gravity
  Surge – Not occurring, neutral
Stability

## Slide 30: Wave Diffraction – Excitation Force
Force in the body due to the presence of the wave
Incident wave
  Froude Krylov Force
Scattered wave
Diffraction = Incident + scattered wave
  Excitation Force
Degrees of Freedom

## Slide 31: Added Mass – Hydrodynamic Inertia
Force as a function of acceleration
Represents the inertia of the accelerated water mass
Frequency independent when body is deeply submerged
Frequency dependent when body is near water surface
Cross coupling effects between different degrees of freedom
Cross coupling effects between degrees of freedom of different bodies
Newman, Marine Hydrodynamics, 1977

## Slide 32: Added Mass – Hydrodynamic Inertia
Force as a function of acceleration
Represents the inertia of the accelerated water mass
Frequency independent when body is deeply submerged
Frequency dependent when body is near water surface
Cross coupling effects between different degrees of freedom
Cross coupling effects between degrees of freedom of different bodies
Newman, Marine Hydrodynamics, 1977

## Slide 33: Wave Radiation – Hydrodynamic Damping
Force as a function of velocity
Represents the energy consuming damping due to the radiation of a wave
Frequency dependent
Zero when body is deeply submerged
Cross coupling effects between different degrees of freedom
Cross coupling effects between degrees of freedom of different bodies
Newman, Marine Hydrodynamics, 1977

## Slide 34
Wave Energy Conversion

## Slide 35: Energy Distribution
Single Mode Sea-State
Bi-Modal Sea-State

## Slide 36: Ocean Wave Dynamics – Dispersion Relation
Quick explanation
Formular
Graph
Meaning
Ref: https://folk.ntnu.no/oivarn/hercules_ntnu/LWTcourse/indexA.htm

## Slide 37: Wave Energy Absorption
Jorgen Hals

## Slide 38: Power Takeoff – Damping & Restoring
Power Take-Off Functions
  Provide interaction with the wave absorbers to extract energy from ocean waves and convert to other secondary energy form (e.g., mechanical)
  Convert the secondary energy form to the desired energy form (e.g., electrical)
Power Take-Off Capabilities
  Energy conversion through damping force – in phase with velocity
  Energy storage through restoring force – in phase with displacement

## Slide 39
Technology

## Slide 40: Technology – Concept Classification
Location
Orientation

## Slide 41: Technology – Concept Classification
Mechanism of Extraction

## Slide 42: Technology – Concept Classification
Reactional Reference
Motion Degrees of Freedom in Coordinate System

## Slide 43: Technology – Concepts – Heaving Point Absorber

## Slide 44: Technology – Concepts – Surging Bottom Hinged Flap

## Slide 45: Technology – Concepts – Hinged Barges

## Slide 46: Technology – Concepts – Oscillating Water Column

## Slide 47: Technology – Concepts – Overtopping Device

## Slide 48: Technology – Energy Conversion Chain – Power Take-Off
A. Têtu
Different paths for wave energy to electricity conversion

## Slide 49
Benchmark Studies

## Slide 50: Wave Energy Absorption – Benchmark Study
Quantities of Interest
Performance Metrics

## Slide 51: Wave Energy Absorption – Benchmark Study

## Slide 52: Wave Energy Absorption – Benchmark Study

## Slide 53: Wave Energy Absorption – Benchmark Study

## Slide 54
Technology Development Methods

## Slide 55: System Modelling and Simulation
Wide variety of system models and simulation tools to be selected for use case
More to come …

## Slide 56: Wave Basin Testing and Validation
Fundamental Concept
Power Absorption Code Validation
Survival Testing
Advanced Control Testing
Sophisticated Direct Generation Power Take-Off

## Slide 57: Bench and Laboratory Testing and Characterization

## Slide 58: Open Water Demonstration – Test Sites
EU
US: Hawaii & Pacific Coast

## Slide 59
Technology Development History

## Slide 60: Early Developments
First patent is reported to have been filed as early as 1799 by Girard and since then patent numbers are well in the thousands
First oscillating water column designed by Palme in 1920
Early developments in the US include 1898 patent by Wright

## Slide 61: Early Developments
First commercial application of wave energy:
In 1940s, Japanese inventor, Yoshio Masuda, lead substantial research and invented, designed and build floating of oscillating water column device to generate power for navigation buoys.
Commercialization in large numbers in Japan from 1965 and later in USA.

## Slide 62: Oscillating Water Column Devices

## Slide 63: Oscillating Water Column Devices

## Slide 64: Oscillating Water Column Devices

## Slide 65: Floating Oscillating Water Column Devices

## Slide 66: Oscillating Water Column Devices Turbines

## Slide 67: Salter Duck

## Slide 68: Salter Duck
Survivability
Ref: Salter, S. Wave energy: Nostalgic Ramblings, future hopes and heretical suggestions. J. Ocean Eng. Mar. Energy 2, 399–428 (2016). https://doi.org/10.1007/s40722-016-0057-3

## Slide 69: Salter Duck

## Slide 70: Salter Duck … Weptos

## Slide 71: Pelamis

## Slide 72: Pelamis

## Slide 73: Pelamis

## Slide 74
Challenges & Motivation & Solutions

## Slide 75: Technology – Development Challenges: Cost

## Slide 76: Technology – Development Challenges: Risk

## Slide 77: Technology – Development Challenges: Time

## Slide 78: Technology – Development Challenges: Innovation

## Slide 79
Challenges & Motivation & Solutions

## Slide 80: Technological Evolution vs Intelligent Design
• Early convergence of concepts,
• Technical feasibility, industrial production and market opportunity at all and growing scales,
• Availability of technological knowhow & experience in theory, design, production & operation of very similar industrial applications,
• Cheap and easy access (onshore) to operating system, allowing gradual failure rate reduction during commercial operations.
Technological Evolution
Intelligent Design
• Large spectrum of different converter system concepts,
• Strongly decreased market opportunity at reduced scales,
• Limited transferability of technological experience, design, production and operation of similar industrial applications,
• Expensive and delayed access to operating system (offshore), prohibiting high failure rates from the onset of commercial operations.
Wind Energy
Wave Energy

## Slide 81: Learnings, Methods and Tools to Solutions
Technology Development Strategy, Methods and Tools
  Development Protocols
  Cost, Time and Risk Reduction
Techno-Economic Assessment
Significant improvement in Modelling, Simulation of Dynamics, Loads and Stresses
System Optimization & Co-Design
Marine Operations Modelling
Novel Power Conversion Systems
Advanced Manufacturing Methods
Identification of Alternative Markets
  Blue Economy
  High Impact Applications
Design Paradigm Shifts

## Slide 82: Technology – Possibility for Paradigm Shift?
SBM Offshore
Pelamis

## Slide 83
Tuning Wave Energy Converters & Design of Oscillating Wave Surge Converters

## Slide 84: Developing Understanding
Tuning
Motion
Constraints
Natural
Bandwidth

## Slide 85: Tuning
Obtaining resonance is critical for good performance
x5

## Slide 86: Tuning and Motion Constraints
Motion constraints
for narrow-banded WEC
Increasing motion
constraints
Motion constraints
for broad-banded WEC
Increasing motion
constraints

## Slide 87: Natural Bandwidth

## Slide 88: WEC Control Value Matrix
Natural Bandwidth
Constraint
Wide
Narrow
High
Low
OWSC
Heaving buoy
Increasing benefit
of advanced control

## Slide 89: Designing an Oscillating Wave Surge Converter
A preliminary investigation

## Slide 90: Oyster 1

## Slide 91: Oyster 800

## Slide 92: Wave Torque
Torque
Velocity
Power

## Slide 93: Effect of Water Depth

## Slide 94: Effect of Water Depth

## Slide 95: Effect of Water Depth

## Slide 96: Effect of Water Depth

## Slide 97: Effect of Flap Submergence
12.0 m

## Slide 98: Effect of Flap Submergence
0.1 m
12.0 m

## Slide 99: Effect of Flap Submergence
0.2 m
12.0 m

## Slide 100: Effect of Flap Submergence
0.5 m
12.0 m

## Slide 101: Effect of Water Width

## Slide 102: Tuning
Torque
Velocity
Power

## Slide 103: OSWC Tuning & Buoyancy
12.0 m Water depth
3.0 m Hinge height
2.0 m Flap thickness
300 kg/m3 Flap density
10.0 sec Natural period
Flap submerged
Flap surface-piercing

## Slide 104: Effect of Tuning & Motion Constraints
Unconstrained
12.0 m wide submerged flap
7.4 m high flap
2.0 m thick flap
10.0 sec. natural period
1.0 m wave amplitude

## Slide 105: Effect of Tuning & Motion Constraints
Constrained
12.0 m wide submerged flap
7.4 m high flap
2.0 m thick flap
10.0 sec. natural period
1.0 m wave amplitude
30 deg. max. rotation

## Slide 106: OSWC Design Space - Tuned
Narrow surface-piercing flap
Small wave torque
Motion constrained
Wide submerged flap
Small wave torque
Motion constrained
Flap on a stalk
Large structural task
High buoyancy force

## Slide 107: Untuned OWSC
18.0 m wide surface-piercing flap
2.0 m thick section
12.0 m water depth
Optimum damping
1.0 m wave amplitude
30 deg max. rotation

## Slide 108: Tuned vs Untuned OSWCs
Tuned
Higher theoretical power capture
Untuned
Lower theoretical power capture
Complexity
Simplicity
High wave forces
High buoyancy forces

## Slide 109: Alternative OWSC Configuration
How may this change our perspective?
Wave force
Motion constraints
Natural bandwidth
Tuning
Power capture

## Slide 110
Conversion Chain Control Co-Design
Notes: Brittany

## Slide 111: System Optimization & Power Flows
“Classical” approach Falnes et. al, 1980s
Absorbed power
Useful power
Hydro-mechanical body
Load (Controller)
Power take off
losses

## Slide 112: System Optimization & Power Flows
Impedance matching network
Bi-conjugate
impedance matching as framework for concurrent
PTO & control design
 WEC control co-design
Power in
Power out
Expanded framework
Hydro-mechanical body
Load (Controller)
Power take off dynamics
losses
“Classical” approach Falnes et. al, 1980s

## Slide 113: System Optimization & Power Flows
Power in
Power put
Load
Wave-body interactions
Impedance matching network

## Slide 114: System Optimization & Power Flows
Absorbed power
Mech power
Elec power
Input (well) matched
Load (Controller)
Load (Controller)

## Slide 115
Overall Objective
Notes: Brittany

## Slide 116: System Optimization Technology & Farm Operations
Wave Energy Converter & Farm System Models

## Slide 117: Questions
Notes: Carrie